BOSCH - VW DISTRIBUTOR INFORMATION

TUNE UP PART NUMBERS – mostly USA

Many sources were used, the main ones were:

-BOSCH Fast Moving Parts Catalog AE2000-1i 06/1968, 01/1971, 03/1972, 11/1973, 01/1975

- Bosch Ignition Parts catalogs from 1978, 1983, 1984 and 1996

- Volkswagen Parts Books

- Volkswagen Technical Bulletins - from various sources.

- some other various books, including The Car of the Century by JT Garwood.

Main focus in this chart is the 1960-1980 era

Chart groupings largely based on the vacuum canisters               Rev. 07-27-2021

| BOSCH DISTRIBUTOR NUMBER | VW PART NUMBER | APPLICATION | POINTS | CNDNSR | CAP | ROTOR | VACUUM CANISTER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 231 115 040 VJUR 4 BR8 | 111905205C | 36HP | 01002 | 1237330055 02170 | 03019 | 1234332072 (04008) | 07002 |
| 0 231 137 001 ZV/JUR 4 R 1 | 141905205 | 08/59 – 01/60 Ghia | 1237013025 | 1237330067 | 03019 | 1234332072 (04008) | 1237121 200 |
| 0 231 138 001 ZV/PAU 4 R 1 | 111905205H | 02/60 – 07/60 Ghia | 01006 | 1237330041 02006 | 03037 | 04010 | 07015 NOTE: vacuum canister superseded to this number |
| 0 231 139 002 ZV/PAU 4 R 2 | 113905205A | 1961 Type 1-2 | 01006 | 1237330041 02006 | 03037 | 04010 | 07015 |
| ZV/PAU 4 R 4 ZV/PAU 4 R 6 | 311905205 | 1961-63 Type 3 1500 |  |  |  |  |  |
| 0 231 139 005 ZV/PAU 4 R 5 | 113905205A | 1962-64 Type 1-2 |  |  |  |  |  |
| 0 231 150 001 ZV/JCU 4 R 3 | 341905205 | 1964 Type 3 1500S | 01002 | 02006 | 03002 | 04006 | 341905271 |
| 0 231 137 002 | ? ? | 2/64 – 3/65 Type 2 | 01009 | (02007) 02069+ | 03001 | 04006 | 07016 |
| 0 231 137 005 ZV/JU 4 R 6 | 111905205N | 1965 Type 1-2 1966 Type 3 1500A |  |  |  |  |  |
| ZV/JU 4 R 3 | 111905205L | mid 64-65 Type 1 03/64 - 04/65 Type 2 64-66 Type 3 1500N |  |  |  |  |  |
| 0 231 147 002 ZV/JU 4 R 8 | 111905205M |  |  |  |  |  |  |
| 0 231 147 006 | 311905205D | 1965 Type 3 1500S | 01009 | (02007) 02069+ | 03001 | 04006 | 07017 |
| 0 231 137 007 | 311905205E | 1965 Type 3 1500S |  |  |  |  |  |
| 0 231 137 013 | 311905205F | 1966 Type 3 1600TL |  |  |  |  |  |
| 0 231 137 009 0 231 137 011. 0 231 137 015 0 231 137 017 | 113905205K 131905205 315905205 311905205G | 1966-67 Type 1 1966-67 Type 2 1967 Type 3 1967 Type 3 |  |  |  |  |  |
| 0 231 137 031 | 315905205B | late 1968 Type 3/onward and Service Replacement for others with 07017 canister | 01013 | (02007) 02069+ | 03010* | 04012 |  |
| 0 231 137 033 | 311905205Q | 1969 non US T3 1600 |  |  |  |  |  |
| 0 231 163 001 0 231 163 003 0 231 163 008 0 231 163 018 | 311905205L 311905205M 311905205AB 311905205AC | 1968-69 Type 3 MT 1969-70 Type 3 AT 1970 Type 3 MT 1971 Type 3 MT | 01011 | 02039 | 03001 | 04006 | 07022 |
| 0 231 167 014 0 231 167 016 | 311905205T 311905205AA | 1970 Non-USA Type 3 | 01009 | 02071 | 03001 | 04006 | 311905271C |
| 0 231 115 056 0 231 115 058 0 231 115 078 0 231 115 073 0 231 115 082 | 113905205P 311905205P 113905205AA 113905205AB 113905205AC | 1968 Type 1 AT Non-US Type 3 AT 1969-70 Type 1 AT 1969 Type 1 AT 1970 Type 1 AT | 01011 | 02021 | 03001 03001 03010* 03010* 03010* | 04006 04006 04033** 04033** 04033** | 07023 |
| 0 231 137 021 0 231 137 027 0 231 137 035 0 231 137 037 0 231 137 039 | 113905205M 211905205N 113905205T 211905205P 111905205AA | 1968 Type 1-2 1968 T2 1600 non-US 1969-70 Type 1-2 1969 T2 1600 non-US 1970-74 1200 & service replacement for the others with the 07024 canister | 01013 | 02069+ | 03001 03001 03010* 03010* 03010* | 04006 04006 04033** 04033** 04033** | 07024 |
| 0 231 146 081 0 231 115 077 | 021 905 205 021 905 205B | 1969 411 Man/Carb V 1969 411 Auto/Carb V | 01011 | 021905295 | 03010* | 04033** | 021905271 |
| 0 231 167 018 0 231 167 020 | 021 905 205A 021 905 205C | 1970-71 411 Manual W 1970-71 411 Auto W | 01011 | 02071 | 03010* | 04033** | 021905271A |
| 0 231 163 011 | 022905205H | 1971-72 Type 4 AT | 01011 | 02054 | 03010* | 04033** | 07042 |
| 0 231 163 016 | 311905205AD | 1971 Type 3 AT | 01011 | 02039 | 03001 | 04006 | 07044 |
| 0 231 163 027 0 231 163 029 | 311905205AG 311905205AH | M1972-73 Type 3 MT M1972-73 Type 3 AT | 01011 | 02054 | 03001 | 04006 | 07052 |
| 0 231 168 015 0 231 170 186 | 043905205L 043905205K | 1976+ Type 2 1970s-1980s non-US T1 | 01011 |  | 03010 | 04021 | 07058 |
| 0 231 170 034 0 231 170 036 0 231 168 001 | 043905205 043905205A 043905205B | L73-74 Type 1 49 MT L73-74 Type 1 49 AT non-US 70s Type 2 1.6 | 01011 | 02074 | 03010 | 04033 | 07059 |
| 0 231 168 001 (Mex) 0 231 170 034 (Mex) | 043905205ZB 043905205 | Mexican made SVDA | 01011 | 02046 02054 | 03010 | 04033 | 07059 |
| 0 231 170 093 0 231 170 093 0 231 168 005 0 231 170 093 | 022905205S 022905205S 021905205P 022905205S | 1974 Type 4 74, 76-78 Type 2 Cal 1976-79 Type 2 49 1980-83 Type 2 49 | 01052 01052 01011 01052 | 02074 | 03010 | 04033 | 07060 |

| BOSCH DISTRIBUTOR NUMBER | VW PART NUMBER | APPLICATION | POINTS | CNDNSR | CAP | ROTOR | VACUUM CANISTER |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 231 167 012/013 | 113905205AD | 1970 Type 1 AT | 01011 | 02054 | 03010* | 04033** | 07083 |
| 0 231 172 005/006 0 231 172 007/008 0 231 174 001/002 0 231 174 005 | 022905205A 022905205E 022905205F 022905205F | 1970 411E and 411EL W Oct-Dec 1970 914 W Jan 1971-72 914 1973 914 | 01011 | 02071 02071 02054 | 03010* | 04033** | 07085 |
| 0 231 167 048/049 | 113905205AJ | 1971 Type 1 MT Vac Can superceded to: | 01011 | 02054 | 03010* | 04033** | 07091 (07223) |
| 0 231 173 001 0 231 167 055 0 231 167 053 | 211905205Q 211905205Q 113905205AH | 1971 Type 2 1971 Type 2 1971-73 Type 1 AT* | 01011 | 02054 | 03010* | 04021 04033** 04033** | 07092 |
| 0 231 115 094 | 113905205AM | 1972 Non-US Type 1 AT | 01011 | 02054 | 03010* | 04033** |  |
| 0 231 146 101 0 231 180 001 | 113905205AL 211905205S | 1971-72 Non USA Type 1-2 MT | 01011 | 02054 | 03010* | 04033** | 1237121 461 |
| 0 231 172 009 0 231 172 011. | 311905205AE 311905205AF | 1972 Type 3 MT 1972 Type 3 AT | 01011 | 02054 | 03001 | 04006 | 07100 |
| 0 231 173 005 0 231 173 007 | 021905205E 021905205F | 1972 Type 2 MT 1973 Type 2 AT | 01011 | 02071 | 03010 | 04016 | 07101 |
| 0 231 167 070 | 113905205AN | 1972-73 Type 1 1973-74 Thing 49 | 01011 | 02054 | 03010 | 04033 | 07102 |
| 0 231 174 007 | 022905205Q | 1973 914 | 01011 | 02054 | 03010 | 04030 | 07109 |
| 0 231 173 009 | 021905205J | 1973 Type 2 MT | 01011 | 02071 | 03010 | 04016 | 07113 |
| 0 231 176 028 0 231 176 044 | 043905205C 043905205H | L73-74 Type 1 Cal MT 1973-74 Thing Cal 1975-79 Type 1 | 01011 | 02074 | 03010 | 04033 | 07114 |
| 0 231 181 005 | 021905205N | 1974 Type 2 49 MT | 01011 | 02074 | 03010 | 04016 | 07115 |
| 0 231 181 003 | 021905205Q | 1974 Type 2 49 AT | 01011 | 02074 | 03010 | 04016 | 07116 |
| 0 231 176 033 | 043905205D | L73-74 Type 1 Cal AT | 01011 | 02074 | 03010 | 04033 | 07118 |
| 0 231 181 007 0 231 181 009 | 021905205S 022905205AA | 1974 Type 2 49 AT 1974 914 | 01011 | 02074 | 03010 | 04016 04030 | 07121 |
| 0 231 176 048 0 231 181 012 | 021905205AB 022905205AB | 1975 Type 2 Cal MT + 914 1975 Type 2 49 MT | 01011 | 02074 | 03010 | 04033 04016 | 07125 |
| 0 231 176 053 | 043905205J | 1975-79 Type 1 AT | 01011 | 02074 | 03010 | 04033 | 07126 |
| 0 231 176 055 0 231 181 014 | 021905205AC 022905205AC | 1975 Type 2 Cal AT 1975 Type 2 49 AT | 01011 | 02074 | 03010 | 04033 04016 | 07127 |
| 0 231 174 011 0 231 172 021 | 039905205A 039905205B | 1974 914 1975 914 | 01011 | 02054 | 03010 | 04030 | 07128 |
| 0 231 167 029 | 113905205AE | 1970 Type 1 AT | 01011 | 02054 | 03010 | 04033 | 07138 |
| 0 231 172 019 0 231 174 009 | 022905205P 039905205 | 1973 Type 4 1973 914 | 01011 | 02054 | 03010 | 04033 04030 | 07140 |
| 0 237 022 009 | 039905205C | 1979-83 Type 2 Cal | n/a | n/a | 03010 | 04038 | 07163 |
| 0 237 022 025 0 237 022 045 | 025905205D 025905205K | late 1983-84 Type 2 1985 Type 2 | n/a | n/a | 03010 03212 | 04038 | 07212 |
| Distributors with only Centrifugal Advance |
| 0 231 129 019 VJR 4 BR 8 | 211 905 205E | 1955-59 Type 2 | 01001 | 02170 | 03019 | 04008 | n/a |
| 0 231 129 010 VJR 4 BR 25 | 211 905 205F | 1959-60 Type 2 | 01001 | 02170 | 03019 | 04008 |  |
| 0 231 178 003 0 231 178 009 9 230 081 094 | 126 905 205 none none | Industrial Bosch 009 chromed 009 | 01030 01030 01030 | 02086 # 02086 # 02086 # | 03010 03010 03010 | 04033 04033 04033 |  |
| 9 230 081 050 | none | Bosch 050 | 01030 | 02086 # | CAP - 9 231 081 413 ROTOR - 9 231 081 628 CNDSR – 9 231 081 687 |

Latest revision: 02-01-21 Andy T.  “glutamodo” – w/some input and verification from Everett, Tasb and Ratwell.

VW TUNE UP PARTS – BOSCH PART NUMBER CROSS-REFERENCE

| SHORT | LONG | Volkswagen | SHORT | LONG | Volkswagen |
| --- | --- | --- | --- | --- | --- |
| 01 001 | 1 237 013 000 | 111 998 051 | 02 071 | 1 237 330 247 | 311 905 295B 021 905 295A |
| 01 002 | 1 237 013 006 | 111 998 053 | 02 074 | 1 237 330 252 | 028 905 295B |
| ? | 1 237 013 025 | 111 998 055 | 02 086 | 1 237 330 280 #1 237 330 342 9 231 083 017 |  |
| 01 006 | 1 237 013 026 | 111 998 057 | 02 170 | 1 237 330 055 | 111 905 295 |
| 01 009 | 1 237 013 039 9 231 081 332 | 111 998 059 | 03 001 ZVS74Z6 | 1 235 522 027 | 111 905 207C |
| 01 011 | 1 237 013 044 (also: 1 237 013 051) | 311 998 063 059 998 015 059 998 051 | 03 002 ZVS74Z8 | 1 235 522 031 | 341 905 207 |
|  |  |  | 03 010 | 1 235 522 056 | 113 905 207B/C |
| 01 013 | 1 237 013 057 | 111 998 063 | 03 019 ZVS75Z6 | 1 235 522 107 | 111 905 207B |
| 01 030 | 1 237 013 092 |  |  | 1 235 522 183 | 113 905 207A |
| 01 038 | 1 237 013 108 | 058 998 051A | 03 037 ZVVS5Z2 | 1 235 522 232 | 113 905 207 |
| 01 052 | 1 237 013 130 | 059 998 051B | 03 212 | 1 235 522 370 | 027/055 905 207 |
|  |  |  | 04 006 ZVVT5Z9 | 1 234 332 082 | 111 905 225F |
| 02 006 | 1 237 330 041 1 237 330 067 | 113 905 295 | 04 008 |  | 111 905 225C |
| 02 007 | 1 237 330 069 | 111 905 295A | 04 010 ZVVT7Z9 | 1 234 332 100 | 113 905 225 A |
|  |  |  | 04 111 ZVVT7Z10 | 1 234 332 101 | no-resistor version of above |
|  | 1 237 330 096 | 311 905 295A | 04 012 | 1 234 332 107 | 113 905 225E |
|  | 1 237 330 110 | 311 905 295 | 04 016 ZVVT12Z2 | 1 234 332 144 | 021 905 225 |
| 02 021 | 1 237 330 117 1 237 330 137 | 113 905 295B 059 905 295 | 04 021 | 1 234 332 192 | 211 905 225B |
| 02 039 | 1 237 330 191 |  | 04 030 | 1 234 332 207 |  |
| 02 054 | 1 237 330 220 | 311 905 295C | 04 033 | 1 234 332 215 | 043/055/181 905 225 |
| 02 069 | 1 237 330 245 | 311 905 295A | 04 038 | 1 234 332 300 | 055 905 225B |

NOTES:

If a black distributor cap is desired to go in place of the orange 03010 (1 235 522 056) use BOSCH part number 03 172 (9 231 081 711).

*Originally the 1969-early 70s distributors with the tall cap/rotor, were listed as taking a 1235522183-113905074A  distributor cap, now superseded to the 03010.

**The 04012 rotor was used on many cars from 1969-73 and is sometimes still listed as the part for them, however, the 04033 has all but superseded it now and is shown in place of the 04012 on the chart.

The 04033 and 04012 also fit in place of RPM-limiting rotors such as the 04016.

The 04111 unscreened (no resistor) rotor was sometimes listed in place of the 04010

01011 Points will fit in place of 01030 and 01052 - wire length and/or spring tension are different though.

# Apparently, for the 009 centrifugal style distributors, some vendors are now selling the Bosch 1 237 330 342 instead of the 02 086 condenser.

+Condensers from circa mid 1964 through 1970 on many distributors routed through a plastic plug in the bottom of the distributor.  These distributors have a middle BOSCH number of 137 and 147.   Several very similar condensers were used during this time.  The main difference between them is the length of the distributor wire, otherwise their fit and function should be the same.  Consequently, the long-wire 02069 (1 237 330 245) has become the standard replacement for all of them.  I’ve heard it claimed that the last 3 digits of these numbers indicates the length of that wire.    A list of these includes the:

1 237 330 069 (02007) from mid 64 thru 1965 Type 1/2

1 237 330 079 on 1966 type 3 1600TL

1 237 330 089 on the 1966-67 Type 1/2

1 237 330 096 on 1967 type 3s.

1 237 330 119 on 1968 type 1s

1 237 330 120 – unknown application, but fits in place of the ones above.

Condensers from the late 60s onward on SVDA and DVDA distributors exited out the side of the distributor housing in a round or square hole.

02 021 – Early round-hole style, short wire – 185 mm.

02 054 – Later round-hole style, longer wire – 420 mm.

02 071 -  Early round-hole style, short wire – 210 mm.

02 074 – Square-hole style – stock VW units.

02 086 – Square-hole style – for 009.

Bosch Tune Up Kits.  Bosch marketed blister-packaged Ignition Kits (points and condenser) and Cap & Rotor Kits.  These are the ones listed in the 1969, 1971, 1978 and/or 1983 catalogs)

| IK 1 | 1955-60 Type 1 36HP - 1 237 013 006 & 1 237 330 055 |
| --- | --- |
| IK 4 | 1955-59 Type 2 "019" - 1 237 013 000 & 1 237 330 055 |
| IK 9 | 01 006 & 02 006 |
| IK 19 | 01 009 & 02 007 |
| IK 20 | 01 009 & 02 069 (early 70s kits contained 1 237 330 089 condenser) |
| IK 22 | 01 013 & 02 069 (early 70s kits contained 1 237 330 119 condenser) |
| IK 23 | 01 011 & 02 039 (early 70s kits contained 1 237 330 117 condenser) |
| IK 65 | 01 009 & 1 237 330 069 (superseded in mid 70s by the IK20 Kit) |
| IK 68 | VW distributor (see below) 1 217 999 012 & 1 237 999 011 |
| IK 71 | 01 011 & 02 021 |
| IK 81 | 01 011 & 02 054 |
| IK 97 | 01 011 & 02 074 |
| IK 900 | 01 030 & 02 086 - for Bosch 009 Centrifugal Distributor |
| CR 1 | 03 037 & 04 010 (or possibly 04 111) |
| CR 2 | 03 001 & 04 006 |
| CR 3 | 03 010 & 04 012 |
| CR 33 | 03 010 & 04 033 |
| CR 86 | 03 010 & 04 038 |

Dust Shield sealing discs:  Often discarded long ago, here is a partial listing:

111 905 241 – for the early 50s distributors

111 905 241C -

111 905 241D - Bosch 1230500019

113 905 241  -  Bosch 1230500021 – Fits the ZV/PAU 4Rx  large-diameter units

111 905 241E - Bosch 1230500093

111 905 241F - Bosch 1230500096 (probably the most commonly seen one)

- Bosch 1230500147

Note: it’s been pointed out that despite Type 1 and Type 2 parts books clearly stating the 1119052041E is for many smaller diameter 1967/older Bosch distributors, it seems to better fit the GL units talked about in the following section, despite those units having a part number of their own for a sealing disc.

The "VW" distributors (not marked as, but made by Garbe Lahmeyer) from the 1950s, up into the early 70s. Some vacuum advance models have an adjustable vacuum advance spring operated mechanism allowing them to be matched to various distributors.

Vacuum advance distributors:

111 905 207 B 1950's through 1960 type 1 
111 905 207 C 1964-1968 type 2 
113 905 207 1961-1964 type 1 & 2 
113 905 207 A 1969-1972 type 2

Mechanical advance distributors:

211 905 205 B 1950's type II 
211 905 207 1960's type II

|  | VW number | Bosch Number | notes |
| --- | --- | --- | --- |
| CAP | 211 905 207 | 1 235 999 020 |  |
| ROTOR | 211 905 225 | - | early, no resistor |
| ROTOR | 211 905 225 A | - | early, with resistor |
| ROTOR | 113 905 225 B | 1 234 999 014 | late, with resistor |
| CONDENSER | 211 905 295 | 1 237 999 011 1 237 330 065 |  |
| POINTS | 111 998 061 | 1 217 999 012 |  |
| Bosch Ignition Kit | - | IK-68 |  |
| Dust sealing disc | 211 905 241 |  |  |

Vacuum Canister	211 905 271 A (non-adjustable)

211 905 271 B (adjustable)

Bosch 999-series tune-up parts for these were re-packaged from other manufacturers

Despite 113 and 211 part numbers, the tune up parts fit all type 1 and type 2 G-L units.

BOSCH VW DISTRIBUTORS

VACUUM CANISTER PART NUMBERS

The 3 (or 4) digit number stamped into the operating arm

of the canister, are usually the end digits of the LONG number.

Many pre-1970 canisters have no number on the operating arm,

or if they do, it may be a date code and not a part number

Main Sources:

- Bosch Parts and Ignition parts catalogs from 1968, 71, 72, 73, 75, 83, 84, and 1996

- Volkswagen Parts Books

-Volkswagen Workshop and Service Manuals

-Misc VW Technical Bulletins  -Car of the Century, J.T. Garwood

| BOSCH DISTRIBUTOR NUMBER | VW PART NUMBER | APPLICATION | VAC CAN SHORT NUMBER | VACUUM CANISTER LONG NUMBER | VACUUM CANISTER VW NUMBER | Total advance crankshaft degrees @ __ mm Hg purple = SVDA green = vacuum-only red = DVDA advance (orange = DVDA retard) |
| --- | --- | --- | --- | --- | --- | --- |
| 0 231 115 040 VJU 4 BR8 | 111905205C | 36HP | 07002 | 1 237 121 | 113 | 111905271A | 8-12° @ 270mm Hg (after March 1956) |
| 0 231 137 001 ZV/JUR 4 R 1 | 141905205 | 08/59 – 01/60 Ghia |  | 1 237 121 | 200 | 141905271 |  |
| 0 231 138 001 ZV/PAU 4 R 1 | 111905205H | 02/60 – 07/60 Ghia (Note: Vacuum Canister number superseded to this one, original had threaded vacuum inlet) | 07015 | 1 237 121 | 201 | 113905271 | 18° (± 3°) @ 50mm Hg |
| 0 231 139 002 ZV/PAU 4 R 2 | 113905205 | 1961 Type 1-2 | 07015 | 1 237 121 | 201 | 113905271 | 18° (± 3°) @ 50mm Hg |
| ZV/PAU 4 R 4 ZV/PAU 4 R 6 | 311 905 205 |  |  |  |  |  |  |
| 0 231 139 005 ZV/PAU 4 R 5 | 113905205A | 1962-64 Type 1-2 |  |  |  |  |  |
| 0 231 137 005 ZV/JU 4 R 6 | 111905205N | 1965 Type 1-2 1966 Type 3 1500A | 07016 | 1 237 121 | 204 | 111905271B | 19° (± 3°) @ 50mm Hg |
| ZV/JU4 R 3 | 111905205L 111905205M | mid 64-65 Type 1 03/64 - 04/65 Type 2 64-66 Type 3 1500N |  |  |  |  |  |
| 0 231 147 002 ZV/JU 4 R 8 |  |  |  |  |  |  |  |
| 0 231 147 006 | 311905205D | 1965 Type 3 1500S |  |  |  |  |  |
| 0 231 137 007 | 311905205E | 1965 Type 3 1500S |  |  |  |  |  |
| 0 231 137 013 | 311905205F | 1966 Type 3 1600TL |  |  |  |  |  |
| 0 231 137 009 0 231 137 011. 0 231 137 015 0 231 137 017 0 231 137 031 | 113905205K 131905205 315905205 311905205G 315905205B | 1966-67 Type 1 1966-67 Type 2 1967 Type 3 1967 Type 3 late 1968/later Type 3 and Service Replacement for others with 07017 canister | 07017 | 1 237 121 | 210 | 311905271 | 25° (± 3°) @ 65mm Hg |
| 0 231 163 001 0 231 163 003 0 231 163 008 0 231 163 018 | 311905205L 311905205M 311905205AB 311905205AC | 1968-69 Type 3 MT 1969-70 Type 3 AT 1970 Type 3 MT 1971 Type 3 MT | 07022 | 1 237 121 | 265 | 311905271A | 8-12° @ 200mm Hg |
| 0 231 115 056 0 231 115 058 0 231 115 078 0 231 115 073 0 231 115 082 | 113905205P 311905205P 113905205AA 113905205AB 113905205AC | 1968 Type 1 AT Non-US Type 3 AT 1969-70 Type 1 AT 1969 Type 1 AT 1970 Type 1 AT | 07023 | 1 237 121 | 277 | 113905271C 311905271B | 5° (± 2°) @ 230mm Hg |
| 0 231 137 021 0 231 137 027 0 231 137 035 0 231 137 037 0 231 137 039 | 113905205M 211905205N 113905205T 211905205P 111905205AA | 1968 Type 1-2 1968 T2 1600 non-US 1969-70 Type 1-2 1969 T2 1600 non-US 1970-74 1200 & service replacement for the others with the 07024 canister | 07024 | 1 237 121 | 279 | 113905271B | 32°-35° @ 80mm Hg |
| 0 231 163 011 | 022905205H | 1971-72 Type 4 AT | 07042 | 1 237 121 | 407 | 022905271B | 11-14° @ 200mm Hg |
| 0 231 163 016 | 311905205AD | 1971 Type 3 AT | 07044 | 1 237 121 | 431 | 311905271D | 2-5° @ 120mm Hg |
| 0 231 146 101 | 113905205AL | non-US 1971-2 Type 1-2 |  | 1 237 121 | 461 | 113905271H | 8-12° @ 180mm Hg |
| 0 231 163 027 0 231 163 029 | 311905205AG 311905205AH | M1972-73 Type 3 MT M1972-73 Type 3 AT | 07052 | 1 237 121 | 505 | 311905271G | 8-12° @ 180mm Hg |
| 0 231 168 015 0 231 170 186 | 043905205L 043905205K | 1976+ non-US Type 2 70s-80s non-US Typ 1 | 07058 | 1 237 121 | 535 |  | 8-12° @ 200mm Hg |
| 0 231 170 034 0 231 170 036 0 231 168 001 | 043905205 043905205A 043905205B | L73-74 Type 1 49 MT L73-74 Type 1 49 AT non-US 1970s Type 2 1600 | 07059 | 1 237 121 | 579 | 043905271 | 8-12° @ 200mm Hg |
| 0 231 170 093 0 231 170 093 0 231 170 093 0 231 170 093 | 022905205S 022905205S 022905205S 022905205S | 1974 Type 4 74, 76-78 Type 2 Cal 1976-79 Type 2 49 1980-83 Type 2 49 | 07060 | 1 237 121 | 581 | 021905271F | 8.5-12° @ 200mm Hg |
| 0 231 167 012 | 113905205AD | 1970 Type 1 AT | 07083 | 1 237 121 | 811 | 113905271D | 8-12° @ 240mm Hg (6-8° @ 170mm Hg) |
| 0 231 172 005 0 231 172 007 0 231 174 001 0 231 174 005 | 022905205E 022905205F 022905205F | 1970 411E 411EL Oct-Dec1969 914 Jan 71-1972 914 1973 914 | 07085 | 1 237 121 | 831 | 022905271A | 11-14° @ 240mm Hg (8-12° @ 160mm Hg) |
| 0 231 167 049 0 231 167 051 | 113905205AJ 113905205AK | 1971 Type 1 MT Vacuum Canister superseded to : | 07091 07223 | 1 237 122 1 237 122 | 851 969 | 113905271F - | 9-12° @ 240mm Hg (11-13° @ 230mm Hg) |
| 0 231 173 001 0 231 167 055 0 231 167 053 | 211905205Q 113905205AH | 1971 Type 2 1971 Type 2 1971-73 Type1 AT * | 07092 | 1 237 121 | 853 | 113905271G | 2-5° @ 240mm Hg (11-13° @ 230mm Hg) |
| 0 231 172 009 0 231 172 011. | 311905205AE 311905205AF | 1972 Type 3 MT 1972 Type 3 AT | 07100 | 1 237 121 | 883 | 311905271E | 8-12° @ 170mm Hg (9-10° @ 260mm Hg) |
| 0 231 173 005 0 231 173 007 | 021905205E 021905205F | 1972 Type 2 MT 1973 Type 2 AT | 07101 | 1 237 121 | 885 | 021905271B | 8-12° @ 200mm Hg (11-15° @ 170mm Hg) |
| 0 231 167 070 | 113905205AN | 1972-73 Type 1 1973-74 Thing 49 | 07102 | 1 237 121 | 889 | 113905271J | 5-8° @ 240mm Hg (11-13° @ 230mm Hg) |
| 0 231 174 007 | 022905205Q | 1973 914 | 07109 | 1 237 121 | 917 |  |  |
| 0 231 173 009 | 021905205J | 1973 Type 2 MT | 07113 | 1 237 121 | 925 | 021905271E | 7-12° @ 180mm Hg (16-18° @ 210mm Hg) |
| 0 231 176 028 0 231 176 044 | 043905205C 043905205H | L73-74 Type 1 Cal MT 1973-74 Thing Cal 1975-79 Type 1 | 07114 | 1 237 121 | 951 | 043905271A | 5-8° @ 240mm Hg (11-13° @ 230mm Hg) |
| 0 231 181 005 | 021905205N | 1974 Type 2 49 MT | 07115 | 1 237 121 | 953 | 021905271G | 7-12° @ 180mm Hg (16-18° @ 210mm Hg) |
| 0 231 181 003 | 021905205Q | 1974 Type 2 49 AT | 07116 | 1 237 121 | 955 |  |  |
| 0 231 176 033 | 043905205D | L73-74 Type 1 Cal AT | 07118 | 1 237 121 | 971 | 043905271B |  |
| 0 231 181 007 0 231 181 009 | 021905205S 022905205AA | 1974 Type 2 49 AT 1974 914 | 07121 | 1 237 121 | 981 | 021905271H | 9-12° @ 220mm Hg (11-13° @ 140mm Hg) |
| 0 231 176 048 0 231 181 012 | 021905205AB 022905205AB | 1975 Type 2 Cal MT + 914 1975 Type 2 49 MT | 07125 | 1 237 121 | 995 | 022905271D | 8-11° @ 240mm Hg (11-13° @ 200mm Hg) |
| 0 231 176 053 | 043905205J | 1975-79 Type 1 AT | 07126 | 1 237 121 | 997 | 022905271E | 8-12° @ 220mm Hg (6-8° @ 200mm Hg) |
| 0 231 176 055 0 231 181 014 | 021905205AC 022905205AC | 1975 Type 2 Cal AT 1975 Type 2 49 AT | 07127 | 1 237 121 | 999 | 022905271F | 3-7° @ 160mm Hg (11-13° @ 210mm Hg) |
| 0 231 174 011 0 231 172 021 | 039905205A 039905205B | 1974 914 1975 914 | 07128 | 1 237 122 | 603 | 039905271 |  |
| 0 231 167 029 | 113905205AE | 1970 Type 1 AT | 07138 | 1 237 121 | 837 | 113905271E | 8-12° @ 240mm Hg (6-8° @ 170mm Hg) |
| 0 231 172 019 0 231 174 009 | 022905205P 039905205 | 1973 Type 4 1973 914 | 07140 | 1 237 122 | 601 | 022905271C |  |
| 0 237 022 009 | 039905205C | 1979-83 Type 2 Cal | 07163 | 1 237 122 | 717 | 039905271B | 9-12° @ 210mm Hg (11-13° @ 210mm Hg) |
| 0 237 022 025 0 237 022 045 | 025905205D 025905205K | 01/83 - 84 Type 2 1985 Type 2 | 07212 | 1 237 122 | 867 | 025905271B | 12-16° @ 270mm Hg (9-11° @ 240mm Hg) |

REPLACEMENT BREAKER PLATE ASSEMBLIES:

This is from the 1968 and 1971 Bosch Catalogs.

Listed were the long-numbers for the replacement breaker plate kits.

| Breaker Plate Assembly | Fits these distributors | application/notes |
| --- | --- | --- |
| 1 237 110 001 | 0 231 129 019 - VJR 4 BR 8 0 231 129 010 - VJR 4 BR 25 |  |
| 1 237 110 002 | 0 231 115 040 - VJUR 4 BR8 |  |
| 1 237 110 034 | 0 231 115 078 and 079 0 231 163 001 |  |
| 1 237 110 046 | 0 231 115 056 |  |
| 1 237 110 064 | 0 231 167 012 and 013 |  |
| 1 237 110 130 | 0 231 137 001 - ZV/JUR 4 R 1 |  |
| 1 237 110 131 | 0 231 138 001 - ZV/PAU 4 R 1 |  |
| 1 237 110 134 | 0 231 139 002 - ZV/PAU 4 R 2 |  |
| 1 237 110 137 | The catalog listing for this is obviously incorrect, it says it’s for the ZVPAU4R5 and for all of the 137 middle-number units, which is impossible |
| 1 237 110 139 | 0 231 137 035 and 036 | this kit can be used to convert the previous 1966-68 distributors from 01009 to 01013 points |

* NOTE:

As an example of the hair pulling frustrating work in trying to correlate and compile data:

Regarding the 0231167053/113905205AH 1971-73 Autostick distributor:

The Fall of 1971 VW parts book says:  (parenthesis notes are mine)

1970:  AD (012) and AE (029) units for M9/M157. (M9=Autostick, M157=USA spec)

1971:  AH (053) for M9/M157 (plus M26 and M27 emissions)

The Bosch Feb 1971 listing shows:

1970: only the 012 (AD) listed.

1971: only the 053 (AH) listed.   This is incorrect also as it says it's for both MT and AT.  Since this was published halfway into model year 1971 a mistake like this is understandable.  It does jibe with the VW parts book as the 012/AD for 1970 and 053/AH for 1971.

Okay, now…. the Bosch 1978 Catalog says:

1970: the 029(AE) for AT with A/C, and 053(AH) for AT.

1971: the 012(AD)

1972: the 053(AH)

That does not match up with the VW parts book.

It should be:

1970: the 012(AD) and 029(AE)

1971 - 73:  the 053(AH)

The vacuum canisters listed in the 1978 catalog also contradict:

The 1970 053 listing, says it had a 07087 canister but then,

The 1972 053 listing, says it had a 07092 canister

Which is correct?  The 07092.  (853)

Why? Speculation: Probably because the 07087 has a long number that ends in 835, I suspect someone typo'd it and then cross-referenced that to the short number.   I don't even know what an 07087 fits... (the 1996 Bosch catalog cross reference chart says it corresponds to VW number 059905271B, which sounds like a water-cooled part, but it doesn't even list it in the "Buyer's Guide" section as an available part.)

| BOSCH (stamped) DATE CODES 1960-2029 |
| --- |
| Year | JAN | FEB | MAR | APR | MAY | JUN | JUL | AUG | SEP | OCT | NOV | DEC | 1Q | 2Q | 3Q | 4Q |
| 1960 | 1R | 2R | 3R | 4R | 5R | 6R | 7R | 8R | 9R | 10R | 11R | 12R |  |  |  |  |
| 1961 | 1S | 2S | 3S | 4S | 5S | 6S | 7S | 8S | 9S | 10S | 11S | 12S |  |  |  |  |
| 1962 | 1T | 2T | 3T | 4T | 5T | 6T | 7T | 8T | 9T | 10T | 11T | 12T |  |  |  |  |
| 1963 | 1U | 2U | 3U | 4U | 5U | 6U | 7U | 8U | 9U | 10U | 11U | 12U |  |  |  |  |
| 1964 | 401 | 402 | 403 | 404 | 405 | 406 | 407 | 408 | 409 | 410 | 411 | 412 | 413 | 414 | 415 | 416 |
| 1965 | 501 | 502 | 503 | 504 | 505 | 506 | 507 | 508 | 509 | 510 | 511 | 512 | 513 | 514 | 515 | 516 |
| 1966 | 601 | 602 | 603 | 604 | 605 | 606 | 607 | 608 | 609 | 610 | 611 | 612 | 613 | 614 | 615 | 616 |
| 1967 | 701 | 702 | 703 | 704 | 705 | 706 | 707 | 708 | 709 | 710 | 711 | 712 | 713 | 714 | 715 | 716 |
| 1968 | 801 | 802 | 803 | 804 | 805 | 806 | 807 | 808 | 809 | 810 | 811 | 812 | 813 | 814 | 815 | 816 |
| 1969 | 901 | 902 | 903 | 904 | 905 | 906 | 907 | 908 | 909 | 910 | 911 | 912 | 913 | 914 | 915 | 916 |
| 1970 | 021 | 022 | 023 | 024 | 025 | 026 | 027 | 028 | 029 | 030 | 031 | 032 | 033 | 034 | 035 | 036 |
| 1971 | 121 | 122 | 123 | 124 | 125 | 126 | 127 | 128 | 129 | 130 | 131 | 132 | 133 | 134 | 135 | 136 |
| 1972 | 221 | 222 | 223 | 224 | 225 | 226 | 227 | 228 | 229 | 230 | 231 | 232 | 233 | 234 | 235 | 236 |
| 1973 | 321 | 322 | 323 | 324 | 325 | 326 | 327 | 328 | 329 | 330 | 331 | 332 | 333 | 334 | 335 | 336 |
| 1974 | 421 | 422 | 423 | 424 | 425 | 426 | 427 | 428 | 429 | 430 | 431 | 432 | 433 | 434 | 435 | 436 |
| 1975 | 521 | 522 | 523 | 524 | 525 | 526 | 527 | 528 | 529 | 530 | 531 | 532 | 533 | 534 | 535 | 536 |
| 1976 | 621 | 622 | 623 | 624 | 625 | 626 | 627 | 628 | 629 | 630 | 631 | 632 | 633 | 634 | 635 | 636 |
| 1977 | 721 | 722 | 723 | 724 | 725 | 726 | 727 | 728 | 729 | 730 | 731 | 732 | 733 | 734 | 735 | 736 |
| 1978 | 821 | 822 | 823 | 824 | 825 | 826 | 827 | 828 | 829 | 830 | 831 | 832 | 833 | 834 | 835 | 836 |
| 1979 | 921 | 922 | 923 | 924 | 925 | 926 | 927 | 928 | 929 | 930 | 931 | 932 | 933 | 934 | 935 | 936 |
| 1980 | 041 | 042 | 043 | 044 | 045 | 046 | 047 | 048 | 049 | 050 | 051 | 052 | 053 | 054 | 055 | 056 |
| 1981 | 141 | 142 | 143 | 144 | 145 | 146 | 147 | 148 | 149 | 150 | 151 | 152 | 153 | 154 | 155 | 156 |
| 1982 | 241 | 242 | 243 | 244 | 245 | 246 | 247 | 248 | 249 | 250 | 251 | 252 | 253 | 254 | 255 | 256 |
| 1983 | 341 | 342 | 343 | 344 | 345 | 346 | 347 | 348 | 349 | 350 | 351 | 352 | 353 | 354 | 355 | 356 |
| 1984 | 441 | 442 | 443 | 444 | 445 | 446 | 447 | 448 | 449 | 450 | 451 | 452 |  |  |  |  |
| 1985 | 541 | 542 | 543 | 544 | 545 | 546 | 547 | 548 | 549 | 550 | 551 | 552 |  |  |  |  |
| 1986 | 641 | 642 | 643 | 644 | 645 | 646 | 647 | 648 | 649 | 650 | 651 | 652 |  |  |  |  |
| 1987 | 741 | 742 | 743 | 744 | 745 | 746 | 747 | 748 | 749 | 750 | 751 | 752 |  |  |  |  |
| 1988 | 841 | 842 | 843 | 844 | 845 | 846 | 847 | 848 | 849 | 850 | 851 | 852 |  |  |  |  |
| 1989 | 941 | 942 | 943 | 944 | 945 | 946 | 947 | 948 | 949 | 950 | 951 | 952 |  |  |  |  |
| 1990 | 061 | 062 | 063 | 064 | 065 | 066 | 067 | 068 | 069 | 070 | 071 | 072 |  |  |  |  |
| 1991 | 161 | 162 | 163 | 164 | 165 | 166 | 167 | 168 | 169 | 170 | 171 | 172 |  |  |  |  |
| 1992 | 261 | 262 | 263 | 264 | 265 | 266 | 267 | 268 | 269 | 270 | 271 | 272 |  |  |  |  |
| 1993 | 361 | 362 | 363 | 364 | 365 | 366 | 367 | 368 | 369 | 370 | 371 | 372 |  |  |  |  |
| 1994 | 461 | 462 | 463 | 464 | 465 | 466 | 467 | 468 | 469 | 470 | 471 | 472 |  |  |  |  |
| 1995 | 561 | 562 | 563 | 564 | 565 | 566 | 567 | 568 | 569 | 570 | 571 | 572 |  |  |  |  |
| 1996 | 661 | 662 | 663 | 664 | 665 | 666 | 667 | 668 | 669 | 670 | 671 | 672 |  |  |  |  |
| 1997 | 761 | 762 | 763 | 764 | 765 | 766 | 767 | 768 | 769 | 770 | 771 | 772 |  |  |  |  |
| 1998 | 861 | 862 | 863 | 864 | 865 | 866 | 867 | 868 | 869 | 870 | 871 | 872 |  |  |  |  |
| 1999 | 961 | 962 | 963 | 964 | 965 | 966 | 967 | 968 | 969 | 970 | 971 | 972 |  |  |  |  |
| 2000 | 081 | 082 | 083 | 084 | 085 | 086 | 087 | 088 | 089 | 090 | 091 | 092 |  |  |  |  |
| 2001 | 181 | 182 | 183 | 184 | 185 | 186 | 187 | 188 | 189 | 190 | 191 | 192 |  |  |  |  |
| 2002 | 281 | 282 | 283 | 284 | 285 | 286 | 287 | 288 | 289 | 290 | 291 | 292 |  |  |  |  |
| 2003 | 381 | 382 | 383 | 384 | 385 | 386 | 387 | 388 | 389 | 390 | 391 | 392 |  |  |  |  |
| 2004 | 481 | 482 | 483 | 484 | 485 | 486 | 487 | 488 | 489 | 490 | 491 | 492 |  |  |  |  |
| 2005 | 581 | 582 | 583 | 584 | 585 | 586 | 587 | 588 | 589 | 590 | 591 | 592 |  |  |  |  |
| 2006 | 681 | 682 | 683 | 684 | 685 | 686 | 687 | 688 | 689 | 690 | 691 | 692 |  |  |  |  |
| 2007 | 781 | 782 | 783 | 784 | 785 | 786 | 787 | 788 | 789 | 790 | 791 | 792 |  |  |  |  |
| 2008 | 881 | 882 | 883 | 884 | 885 | 886 | 887 | 888 | 889 | 890 | 891 | 892 |  |  |  |  |
| 2009 | 981 | 982 | 983 | 984 | 985 | 986 | 987 | 988 | 989 | 990 | 991 | 992 |  |  |  |  |
| 2010 | 001 | 002 | 003 | 004 | 005 | 006 | 007 | 008 | 009 | 010 | 011 | 012 |  |  |  |  |
| 2011 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111 | 112 |  |  |  |  |
| 2012 | 201 | 202 | 203 | 204 | 205 | 206 | 207 | 208 | 209 | 210 | 211 | 212 |  |  |  |  |
| 2013 | 301 | 302 | 303 | 304 | 305 | 306 | 307 | 308 | 309 | 310 | 311 | 312 |  |  |  |  |
| 2014 | 417 | 418 | 419 | 420 | 453 | 454 | 455 | 456 | 457 | 458 | 459 | 460 |  |  |  |  |
| 2015 | 517 | 518 | 519 | 520 | 553 | 554 | 555 | 556 | 557 | 558 | 559 | 560 |  |  |  |  |
| 2016 | 617 | 618 | 619 | 620 | 653 | 654 | 655 | 656 | 657 | 658 | 659 | 660 |  |  |  |  |
| 2017 | 717 | 718 | 719 | 720 | 753 | 754 | 755 | 756 | 757 | 758 | 759 | 760 |  |  |  |  |
| 2018 | 817 | 818 | 819 | 820 | 853 | 854 | 855 | 856 | 857 | 858 | 859 | 860 |  |  |  |  |
| 2019 | 917 | 918 | 919 | 920 | 953 | 954 | 955 | 956 | 957 | 958 | 959 | 960 |  |  |  |  |
| 2020 | 037 | 038 | 039 | 040 | 073 | 074 | 075 | 076 | 077 | 078 | 079 | 080 |  |  |  |  |
| 2021 | 137 | 138 | 139 | 140 | 173 | 174 | 175 | 176 | 177 | 178 | 179 | 180 |  |  |  |  |
| 2022 | 237 | 238 | 239 | 240 | 273 | 274 | 275 | 276 | 277 | 278 | 279 | 280 |  |  |  |  |
| 2023 | 337 | 338 | 339 | 340 | 373 | 374 | 375 | 376 | 377 | 378 | 379 | 380 |  |  |  |  |
| 2024 | 437 | 438 | 439 | 440 | 473 | 474 | 475 | 476 | 477 | 478 | 479 | 480 |  |  |  |  |
| 2025 | 537 | 538 | 539 | 540 | 573 | 574 | 575 | 576 | 577 | 578 | 579 | 580 |  |  |  |  |
| 2026 | 637 | 638 | 639 | 640 | 673 | 674 | 675 | 676 | 677 | 678 | 679 | 680 |  |  |  |  |
| 2027 | 737 | 738 | 739 | 740 | 773 | 774 | 775 | 776 | 777 | 778 | 779 | 780 |  |  |  |  |
| 2028 | 837 | 838 | 839 | 840 | 873 | 874 | 875 | 876 | 877 | 878 | 879 | 880 |  |  |  |  |
| 2029 | 937 | 938 | 939 | 940 | 973 | 974 | 975 | 976 | 977 | 978 | 979 | 980 |  |  |  |  |