| Worldwide VW/Solex Carburetor Types, Carburetor Modification-State / Base Flange Numbers Matching BOSCH Distributor numbers and stock carburetor jetting data. For Upright Bug/BUS/Ghia/Thing 1200-1600 engines, Single-barrel carburetors updated Nov 20 2020 |
| --- |
| 25HP and 36HP engines. Distributors listed are the listed factory originals, Old Bosch #s. |
| Carburetor Type | Matching Distributor Number | Bug Ghia BUS | Engine Size | Approx date of intro | Main Jet | Air Correct Jet | Pilot Jet | Notes |
| 26VFI | VE4BRS383 | Bug | 1131 | 1949 | 120 | 170 | g45 |  |
| 26VFIS | VE4BRS383 | Bug+ BUS | 1131 | 4/50 | 120 | 170 180 | g45 | (timed to 12.5BTDC) |
| 28PCI | VE4BRS383 | Bug+ BUS | 1131 | 10/52 | 105 | 200 190 | g50 | 20mm venturi (timed to 12.5BTDC) |
| 28PCI | VJ4BR2 VJ4BR3 | Bug + BUS | 1200 | 12/53 | 122.5 | 200 | g50 | 6.1:1 compression 22mm venturi |
| 28PCI | VJUR4BR8 | Bug | 1200 | 9/54 | 117.5 | 195 | g50 | 6.6:1 compression begins |
| 28PCI | VJ4BR8 | BUS | 1200 | 9/54 | 117.5 | 195 | g50 |  |
| 28PCI | VJU4BR8 VJUR4BR8 | Ghia | 1200 | 8/55 | 117.5 | 180 | g50 |  |
| 28PCI | ZVJUR4R | Ghia | 1200 | 8/59 | 117.5 | 180 | g50 | With Carb 141129023A |
| 28PCI | ZVPAU4R1 | Ghia | 1200 | 1/60 | 117.5 | 180 | g50 | With Carb 141129023A |
| 28PCI | VJR4BR25 VJ4BR25 | BUS | 1200 | 5/59 | 117.5 | 180 | g50 | With Carb 211129023 |
| 28PCI | ? | Bug | 1200 | 8/60 | 117.5 | 195 | g50 | 1961/newerStandard 36HP model only |
| 1200 (40HP), 1300, 1500 and 1600 engines: |
| Modification State Number | Carb Type | Matching Distributor Number | Bug Ghia BUS | Engine Size | Approx date of intro | Main Jet | Air Correct Jet | Power Fuel: Jet Size and check ball | Notes Pilot jet usually (g)55 unless noted |
| Note: The Modification State number is stamped on the front-of-car side of the carb bowl on older 28PICT-1s and early 30PICT-1, this was later moved to the left base flange across from the throttle attachment |
| none yet | 28PICT | ZVPAU4R2 | Bug | 1200 | 8/60 | 122.5 | 130y | 1.0 with ball |  |
| none yet | 28PICT | ZVPAU4R2 | BUS | 1200 | 6/60 | 122.5 | 145y | 1.0 w/o ball |  |
|  |  |  | Ghia |  | 8/60 |  |  |  |  |
| none yet | 28PICT | ZVPAU4R5 | Bug | 1200 | 8/61 | 122.5 | 130y | 1.0 with ball |  |
| none yet | 28PICT | ZVPAU4R5 | BUS+ Ghia | 1200 | 8/61 | 122.5 | 145y | 1.0 w/o ball |  |
| none yet | 28PICT |  | 6/62 | NOTE: Pipe added to extend upper vacuum advance signal to center of venturi. |
| none yet | 28PICT | ZVPAU4R5 | BUS | 1200 | 1/63 | 122.5 | 145y | 1.0 w/o ball |  |
| none yet | 28PICT | ZVPAU4R5 | BUS | 1500 | 1/63 | 115 | 145y or 150z | 0.70 w/o ball | g45 pilot |
| none yet | 28PICT |  | 5/63 | NOTE- restrictor jet added to vacuum advance nipple |
| VW 4-1(prod) VW 8-1(spares) | 28PICT-1 | ZVPAU4R5 | Bug | 1200 | 11/63 | 122.5 | 130y | 1.0 with ball |  |
|  |  | ZVJU4R3 |  |  | 2/64 |  |  |  |  |
| VW 4-1(prod) VW 8-1(spares) | 28PICT-1 | 111905205M/N | Bug | 1200 | 8/64 | 122.5 | 130y | 1.0 with ball |  |
| NOTE: VW-9 VW-13 | 28PICT-1 | VJUR4BR8 (111905205F) | Dual Cyclone Filters - VW wanted a carb with no upper advance drilling due to the SVDA style distributor, which was timed statically at 12.5BTDC. |
|  |  |  | Bug | 1200 |  | 130 | 170z | NONE | M153 - Carb # 113129023 F or K |
|  |  |  | Ghia | 1200 |  | 130 | 170z | ? | M154 - Carb # 141129023E |
|  |  |  | BUS | 1200 1500 | 8/63 | 122.5 | 130y | ? | M155 - Carb # 141129023H |
| VW 11 | 28PICT-1 |  |  |  | 8/64 |  |  |  | 12V |
| VW 12-1 | 28PICT-1 | ZVPAU4R5 | BUS+ Ghia | 1200 | 11/63 | 122.5 | 145y | 1.0 w/o ball |  |
|  |  | ZVJU4R3 |  |  | 2/64 |  |  |  |  |
| VW 12-1 (prod) VW 15 (spares) | 28PICT-1 | 111905205M/N | BUS+ Ghia | 1200 | 8/64 | 122.5 | 145y | 1.0 w/o ball |  |
| VW 20-1 VW 21-1 VW 22-1 | 28PICT-1 | 111905205M/N | BUS | 1500 | 8/64 | 115 | 150z | 0.70 w/o ball | 6V g45 pilot 12V g45 pilot 6V g45 pilot |
| VW 23 | 28PICT-1 |  | BUS | 1500 | 8/64 |  |  |  | 12V |
| VW 45-1 | 30PICT-1 | 131905205 | BUS | 1500 | 8/65 | 115 | 135z | 0.75 w/o ball | 60 Pilot |
| VW 46-1 | 30PICT-1 | 113905205K | Ghia | 1300 | 8/65 | 125 | 170z | 0.75 w/o ball | Early style throttle return spring |
| VW 47-1 | 30PICT-1 | 113905205K | Bug | 1300 | 8/65 | 125 | 125z | NONE | Early style throttle return spring |
| VW 51-1 | 28PICT-2 | 111905205N 113905205K | Bug 147 | 1200 | 11/65 | 122.5 | 130y | 1.0 with ball | Late style throttle return spring |
| VW 52 | 28PICT-2 |  | Bug | 1200 | 11/65 |  |  |  | SAXOMAT |
| VW 58-1 | 30PICT-1 | 113905205K | Bug+ Ghia | 1300 | 8/65 | 125 | 155z | 0.75 w/o ball | For to use with Dual Cyclone Air Filters 6V |
| VW 60-1 | 30PICT-1 | 131905205 | BUS | 1500 | 12/65 | 117.5 | 135z | 0.75 w/o ball | 6V - 60 pilot |
| VW 61 | 30PICT-1 |  | BUS | 1500 | 8/65 |  |  |  | 12V |
| VW 62 | 30PICT-1 |  |  | 1300 | 8/65 |  |  |  | 12V |
| VW 67 | 28PICT-2 |  |  | 1200 | 11/65 |  |  |  | 12V |
| VW 71 | 30PICT-1 |  | BUS | 1500 | 8/66 |  |  |  | 6V |
| VW 75-1 | 30PICT-1 | 113905205K | Bug | 1300 | 12/65 | 125 | 125z | NONE | Late style throttle return spring |
| VW 76 | 30PICT-1 |  |  |  | 8/66 |  |  |  | 6V- dual air filters |
| VW 77-1 | 30PICT-1 | 131905205 | BUS | 1500 | 8/65 | 115 | 135z | 0.75 w/o ball | 6V - 60 pilot |
| VW 78-1 | 30PICT-1 | 131905205 | BUS | 1500 | 8/65 | 115 | 135z | 0.75 w/o ball | 12V - 60 pilot |
| VW 79-1 | 30PICT-1 |  | BUS | 1500 | 8/65 |  |  | yes | 6V – Austrian? |
| VW 80-1 | 30PICT-1 | 131905205 | BUS | 1500 | 8/66-1/68 | 117.5 | 135z | 0.75 w/o ball | 12V - 60 pilot |
| VW 81-1 | 30PICT-1 | 113905205K | Ghia | 1300 | 12/65 | 125 | 170z | 0.75 w/o ball | Late style throttle return spring |
| VW 82 | 30PICT-1 |  | Ghia? | 1300 |  |  |  |  | M240? |
| VW 83-1 | 30PICT-1 | 113905205K | Bug | 1300 | 8/67 | 125 | 125z | NONE | 12V |
| VW 84-1 | 30PICT-1 | 131905205 | BUS | 1500 | 8/65 | 120 | 145z | 0.75 w/o ball | 6V lower compression - 60 pilot |
| VW 87-1 | 30PICT-1 | 131905205 | BUS | 1500 | 8/65 | 120 | 145z | 0.75 w/o ball | 12V lower compression - 60 pilot |
| VW 89-1 | 28PICT-2 | 113905205K | Bug 147 | 1200 | 8/67 | 122.5 | 140z | 0.75 w/o ball | 6V |
| VW 104-1 | 30PICT-1 | 113905205K | Bug | 1500 | 8/66 | 120 | 125z | 0.50 w/o ball | 6V |
| VW 105-1 | 30PICT-1 | 113905205K | Bug | 1500 | 8/66 | 120 | 125z | 0.50 w/o ball | 12V |
| VW 106-1 | 30PICT-1 | 113905205K | Ghia | 1500 | 8/66 | 120 | 135z | 0.50 w/o ball | 6V |
| VW 107-1 | 30PICT-1 | 113905205K | Ghia | 1500 | 8/66 | 120 | 135z | 0.50 w/o ball | 12V |
| VW 125-1,2 | 30PICT-2 |  | Bug | 1300 | 4/68 | 120 | 125z |  | Non-USA |
| VW 126-1 | 30PICT-2 | 113905205M | Bug | 1500 | 8/67 | x116 | 125z | 0.60 w/o ball | USA |
| VW 126-1 | 30PICT-2 | 113905205M | Ghia | 1500 | 8/67 | x116 | 135z | 0.60 w/o ball | USA |
| VW 126-1 | 30PICT-2 | 113905205M 113905205T | BUS | 1600 | 8/67 | x116 | 125z | 0.60 w/o ball | USA, Typ 2 1600, eng code B5000001-B5116436, M157(emission control) |
| VW 126-2 | 30PICT-2 | 113905205M 113905205T | Bug & Ghia | 1500 | 3/68 | x116 | 125z | 0.60 w/o ball | USA Manual @ H5248586 |
| VW 126-3 | 30PICT-2 | 113905205T | Bug | 1500 | 2/69 | x116 | 125z | 0.60 w/o ball | USA Manual |
| VW 130-1 VW 130-2 | 30PICT-2 |  | Bug | 1300 | 1/68 | 125 | 125z |  | 6V Non-USA |
| VW 131-1 VW 131-2 | 30PICT-2 |  | Bug | 1300 | 1/68 | 125 | 155z |  | 6V – dual air filters Non-USA |
| VW 132-1 VW 132-2 | 30PICT-2 | 113905205K 113905205L 113905205T 113905205AB 113905205AC | Bug | 1300 | 2/68 | X125 | 125z | NONE | Typ1 1300 from F1341000-F1778145 20/02/1968-30/07/1969 12V |
| VW 133 | 30PICT-2 |  | Ghia | 1300 | 1/68 |  |  |  | 6V Non-USA |
| VW 134 | 30PICT-2 |  | Ghia? | 1300 | 1/68 |  |  |  | 6V – M240? |
| VW 135 | 30PICT-2 |  | Ghia | 1300 | 1/68 |  |  |  | 12V |
| VW 136 | 30PICT-2 |  | Ghia | 1300 | 1/68 |  |  |  | 12V |
| VW 137-1 VW 137-2 | 30PICT-2 | 113905205K | Bug | 1300 1500? | 10/67 | 120 | 125z | 0.50 w/o ball | Non-USA (listed for 1300 and 1500) |
| VW 138 | 30PICT-2 |  | Ghia | 1500 | 1/68-1/70 |  |  |  | Non-USA 6V |
| VW 139-1 VW 139-2 | 30PICT-2 | 113905205K | Ghia | 1500 | 8/67 | 120 | 135z | 0.50 w/o ball | Non-USA 12V |
| VW 140 | 30PICT-2 |  | BUS | 1500 | 1/69 |  |  |  |  |
| VW 141 VW 141-4 | 30PICT-2 |  | BUS IND? | 1500 | 1/68 |  |  |  | INDUSTRIAL ENGINE? |
| VW 142 | 30PICT-2 |  | BUS |  | 1/68 |  |  |  |  |
| VW 143 | 30PICT-2 |  | BUS |  | 1/68 |  |  |  |  |
| VW 146-1 | 30PICT-2 | 211905205N 211905205P | BUS | 1600 | 1/68 | 120 | 135z | 0.65 w/o ball | Non-USA From B0019736 to eng B0286760 then went to VW 260-1 |
| VW 164-1 VW 164-2 | 30PICT-2 | 113905205P | Bug | 1300 1500 | 9/67 | 120 | 125z | 0.50 w/o ball | Non-US Autostick |
| VW 167-1 | 30PICT-2 | 113905205P | Bug & Ghia | 1500 | 10/67 | x116 | 125z | 0.60 w/o ball | USA Autostick @H5077366 |
| VW 167-2 | 30PICT-2 | 113905205P | Bug & Ghia | 1500 | 3/68 | x116 | 125z | 0.60 w/o ball | USA Autostick @ H5245666 |
| VW 167-3 | 30PICT-2 | 113905205P | Bug & Ghia | 1500 | 2/69 | x116 | 125z | 0.60 w/o ball | USA Autostick |
| VW 169-1 VW 169-2 | 30PICT-2 | 113905205P | Ghia | 1500 | 9/67 | 120 | 135z | 0.50 w/o ball | Non-USA Autostick |
| VW 170-1 VW 170-2 | 30PICT-2 |  | Bug | 1300 | 1/68 | 125 | 155z |  | Dual Air Filters, 12V |
| VW 171-1 | 30PICT-1 | 113905205K | Bug | 1300 | 8/67 | 125 | 155z | 0.75 w/o ball | Dual Air Filters, 12V |
| VW 172-1 | 30PICT-1 | 211905205N | BUS | 1600 | 8/67 | 120 | 135z | 0.50 w/o ball | Non USA 1600SP, Eng code B0000001-B0019735 |
| VW 181-1 | 28PICT-2 | 113905205K | Bug 147 | 1200 | 8/67 | 122.5 | 140z | 0.75 w/o ball | 12V Non USA |
| VW 196 -2,3,4,5 | 30PICT-2 |  | Bug | 1200 1300 1500 | 8/68 | x116 | 125z |  | Japan, Sweden |

| 1970 Model Year and newer 28 through 34 PICT-2 PICT-3 and PICT-4 upright engines |
| --- |
| Modification State Number (base flange #) | Carb Type | Matching Distributor Number | Bug Ghia BUS | Engine Size | Model year or Date | Main Jet | Air Correct Jet | Pilot (idle fuel) Jet | Notes (all PICT-3/4 carbs have a dual outlet power fuel system) |
| Note: On 30PICT-3, the Mod. State Number might be found stamped into the bowl of the carb next to the volume and air bypass adjustment screws. The number was soon returned to the base flange location. |
| VW 226-1 | 30PICT-3 | 113905205T | Bug & Ghia | 1600 SP | 8/69 | 112.5 | 125z | 65 | USA Manual Aux Fuel 45 |
| VW 227-1 | 30PICT-3 | 113905205AD 113905205AE | Bug & Ghia | 1600 SP | 8/69 | 112.5 | 125z | 65 | USA Automatic Aux Fuel 45 |
| VW 228-1 | 30PICT-2 | 113905205K 113905205L 111905205T | Bug 181 | 1500 | 8/69 | X120 | 125z | 55 | Non-USA Bug H1 engine, from H 1124669 |
| VW 235-1/2 | 30PICT-3 | 113905205T | BUS | 1600 SP | 1970 | 112.5 | 140z | 65 | USA / M157 – Aux Fuel Jet-40 |
| VW 236-1/2 | 30PICT-3 | 113905205M 113905205T | BUS | 1600 SP | 8/69 | X112.5 | 140z | g65 | Typ 2 1600, eng code B5116437-onward, M157(emission control) |
| VW 237-1 | 30PICT-2 | ? | Bug | 1300 | 8/69 | X125 | 125z | 55 | Non-USA Manual F1 engine, from eng F1778146 No power fuel system |
| VW 239-1 | 30PICT-2 | 113905205AC | Bug | 1300 1500 | 8/69 | X125 | 125z | 55 | Non USA Autostick F1 engine, from eng F1778146 No power fuel system |
| VW 240-1 | 28PICT-2 | 113905205K 113905205L 111905205T 111905205AA from D0675001 | Bug | 1200 | 8/69 | 122.5 | 135z | 55 | 6V Non USA |
| VW 241-1 | 28PICT-2 | Same as 240-1 | Bug 147 | 1200 | 8/69 | 122.5 | 135z | 55 | 12V Non USA |
| VW 254 | 30PICT-2 |  | BUG | 1300 | 8/69 |  |  |  | 6V Non USA Dual Air Filters |
| VW 255 | 30PICT-2 |  | BUG | 1300 | 8/69 | 125 | 145z | 55 | 12V Non USA Dual Air Filters |
| VW 257 | 30PICT-2 |  | Ghia | 1300 | 8/69 |  |  |  | 12V Non USA |
| VW 258 | 30PICT-2 |  | Ghia | 1300 | 8/69 |  |  |  |  |
| VW 259-1 | 30PICT-2 | 113905205K 113905205L 111905205T | Ghia | 1500 | 8/69 | X120 | 135z | 55 | Non-USA Ghia H1 engine, from H 1124669 |
| VW 260-1 | 30PICT-2 | 211905205P | BUS | 1600 | 8/69 | x116 | 125z | 55 | From B0286761 |
| VW 262 | 30PICT-2 |  | Ghia | 1500 | 8/69 | 120 | 135z |  | Autostick |
| VW 263-1 | 30PICT-2 | 181905205 | 181 | 1500 | 8/69 | X120 | 125z | 55 | M63 OPTION, MILITARY EQUIPMENT , SUPPRESSION |
| VW 269 | 28PICT-2 |  | BUG | 1200 | 8/67 |  |  |  | 6V Non USA |
| VW 270 | 28PICT-2 |  | BUG | 1200 | 8/67 |  |  |  | 6V SAXOMAT |
| VW 271 | 30PICT-2 |  | BUS | 1600 | 8/69 |  |  |  | 12V |
| VW 275 | 30PICT-2 |  | BUG | 1500 | 01/70-08/70 |  |  |  | 6V |
| VW 276 | 30PICT-2 |  | GHIA | 1300 | 01/70-08/70 |  |  |  | 6V |
| VW 277 | 30PICT-2 |  | BUG | 1300 | 1/70-11/72 |  |  |  | 6V M240 AC Engine |
| VW 278 | 30PICT-2 |  | GHIA | 1500 | 01/70-08/70 |  |  |  | 6V |
| All engines from this point on are 1200 (SP) 1300DP or 1600DP |
| VW 279-1 | 34PICT-3 | 113905205AJ | Bug | 1600 | 1971 | 127.5 | 75z | 60 | USA Manual |
| VW 280-1 | 34PICT-3 | 211905205Q | BUS | 1600 | 1971 | 125 | 60z | 57.5 | USA |
| VW 281-1 | 34PICT-3 | 113905205AH | Bug | 1600 | 1971 | 130 | 75z | 60 | USA Autostick |
| VW 281-2 | 34PICT-3 | 113908205AH | Bug | 1600 | 8/70 | 127.5 | 75z | 60 | USA Autostick |
| VW 281-3 | 34PICT-3 | 113908205AH | Bug | 1600 | 8/71 | 127.5 | 75z | 55 | California autostick |
| VW 281-4 | 34PICT-3 | 113908205AH | Bug | 1600 | 1973 | 127.5 | 75z | 55 | USA Autostick Generator accelerator pump |
| VW 281-5 | 34PICT-3 | 1139008205AH | Bug | 1600 | 1973 | 127.5 | 75z |  | USA Autostick Alternator accelerator pump |
| VW 282- 1,2 | 31PICT-3 | 113905205AJ | Bug | 1300 | 1971 | 125 | 120z | 60 | Non-US manual Aux fuel jet-50, eng AC000001-AC002629 |
| VW 282- 3,4 | 31PICT-3 | 113905205AJ | Bug | 1300 | 1971 | 145 | 170z | 60 | Non-US manual Aux fuel jet-50, From Eng AB000001-AB350000 |
| VW 283-1/2 | 30PICT-3 | 111905205AA | Bug | 1200 | 08/70 | 112.5 | 170z | 55 | Non-USA 1200 12V M88 M610 |
| VW 284-1/2 | 30PICT-3 | 111905205AA | Bug | 1200 | 08/70 | 112.5 | 170z | 55 | Non USA 1200 6V Aux Fuel Jet-40 |
| VW 284-3 | 30PICT-3 | 111905205AA | Bug | 1200 | 08/70 | 112.5 | 170z | 55 | Non USA 1200 6V Aux Fuel Jet-40 |
| VW 285-1 | 30PICT-3 |  |  |  | 1971 |  |  |  | has the redesigned idle cutoff valve |
| VW 289-1 | 34PICT-3 | 113905205AJ | Ghia | 1600 | 1971 | 127.5 | 75z |  | USA Manual |
| VW 290-1 | 34PICT-3 | 113905205AJ | Ghia | 1600 | 8/70 | X127.5 | 80z | 60 | USA Autostick Aux Fuel 42.5 M157(emissions-DVDA, M9(Auto), eng AE000001-AE558000 |
| VW 290-2 | 34PICT-3 | 113905205AN | Ghia | 1600 | 8/71 | X127.5 | 70z | g55 | USA Autostick Aux Fuel 42.5 M157(emissions-DVDA Dizzy), M9(Auto), eng AE558001- |
| VW 290-3 | 34PICT-3 | 113905205AH | Ghia | 1600 |  | x127.5 | 70z | 55 | USA Autostick |
| VW 291-1 | 34PICT-3 | 113905205AJ | Bug | 1600 | 08/70 | x130 |  | 65 | Non-US manual AF engine, M240 |
| VW 291-2 | 34PICT-3 | 113905205AJ | Bug | 1600 | 08/70 | X145 | 130z | 65 | Non-US manual AD engine, eng AD0000001-AD257543 |
| VW 294-1 | 34PICT-3 | 113905205AJ | Ghia | 1600 | 08/70 | 130 |  |  | Non-US manual AF engine, M240 |
| VW 294-2 | 34PICT-3 | 113905205AJ | Ghia | 1600 | 08/70 | X145 | 145z | 65 | Non-US manual AD engine, eng AD0000001-AD257543 |
| VW 297-1 | 34PICT-3 | 113905205AK | Bug | 1600 | 08/70 | 130 |  | 65 | Non-US Autostick AF engine, M240 |
| VW 297-2 | 34PICT-3 | 113905205AK | Bug | 1600 | 08/70 | X145 | 130z | 65 | Non-US autostick AD engine, eng AD0000001-AD257543 |
| VW 298-1 | 34PICT-3 | 113905205AK | Ghia | 1600 | 08/70 | 130 |  |  | Non-US Autostick AF engine, M240 |
| VW 298-2 | 34PICT-3 | 113905205AK | Ghia | 1600 | 08/70 | X145 | 145z | 65 | Non-US autostick AD engine, eng AD0000001-AD257543 |
| VW 299-1/2 | 34PICT-3 | 113905205AJ 211905205R | BUS | 1600 | 08/70 | X140 | 120z | G60 | Non - US AD engine, eng AD0000002-AD290640 |
| VW 302 | 34PICT-3 |  | BUS | 1600 | 08/70 |  |  |  | Non US |
| VW 303-1,2 | 31PICT-3 |  | Bug | 1300 | 08/70 | 125 | 120z |  | Non-USA M52 / M240 eng AC000001-AC002629 |
| VW 303-3,4 | 31PICT-3 |  | Bug | 1300 | 08/70 | 145 | 170z |  | eng AB000001-AB294249 |
| VW 307-1,2 | 31PICT-3 | 113905205AJ | Ghia | 1300 | 1971 | 125 | 140z | 60 | Non-US manual Aux fuel jet-50 M240 |
| VW 307-4 | 31PICT-3 | 113905205AJ | Ghia | 1300 | 1971 | 135 | 170z | 60 | Non-US manual Aux fuel jet-50 |
| VW 310-1 | 31PICT-3 | 113905205AK | Bug | 1300 | 1971 | 125 | 120z | 65 | Non-US autostick Aux fuel jet-50 M240 |
| VW 310-2,3 | 31PICT-3 | 113905205AK | Bug | 1300 | 1971 | 145 | 170z | 60 | Non-US autostick Aux fuel jet-50 |
| VW 311-1 | 31PICT-3 | 113905205AK | Ghia | 1300 | 1971 | 125 | 140z | 60 | Non-US autostick Aux fuel jet-50 M240 |
| VW 311-2,3 | 31PICT-3 | 113905205AK | Ghia | 1300 | 1971 | 135 | 170z | 60 | Non-US autostick Aux fuel jet-50 |
| VW 312-1/2 | 31PICT-3 | 113905205AJ (Eng 1-2699) 113905205AL (eng 2700-3000) | 181 | 1600 | 1971 | 125 | 130z | 65 | Non-US Thing AG engine Aux fuel jet-50 |
| VW 313-1/2 | 31PICT-3 | 181905205 | 181 | 1600 | 1971 | 125 | 130z | 65 | Non-US Thing AG engine Aux fuel jet-50 M63 MILITARY SUPPRESSION |
| VW 320-1,2 | 30PICT-3 | 111905205AA | Bug | 1200 | 08/70 | 112.5 | 170z | 55 | Japan/Sweden 1200 FROM ENG D0675001 12V Aux fuel jet 40 |
| VW 320-3 | 30PICT-3 | 111905205AA | Bug | 1200 | 08/70 | 112.5 | 170w | 55 | Non-US 1200 FROM ENG D0675001 12V Aux fuel jet 40 |
| VW 321-1 | 31PICT-3 | 113905205AJ | Bug | 1300 | 1971 | 125 | 120z | 55 | Non-US manual Aux fuel jet-50, M240, M527 |
| VW 321-2 | 31PICT-3 | 113905205AJ | Bug 181 | 1300 | 1971 | 130 | 110z | 55 | Non-US manual Aux fuel jet-50, M527 181: AG000001-AG002098 |
| VW 322-1 | 31PICT-3 | 113905205AK | Bug | 1300 | 1971 | 125 | 120z | 55 | Non-US autostick Aux fuel jet-50, M240, M527 |
| VW 322-2 | 31PICT-3 | 113905205AK | Bug | 1300 | 1971 | 130 | 110z | 55 | Non-US autostick Aux fuel jet-50, M527 |
| VW 323-1/2 | 31PICT-3 | 113905205AJ | Ghia | 1300 | 1971 | 135 | 140z | 65 | Non-US manual Aux fuel jet-50, M527 VW parts book says 125 main jet |
| VW 324-1 | 31PICT-3 | 113905205AK | Ghia | 1300 | 1971 | 120 | 140z | 65 | Non-US autostick Aux fuel jet-50, M527 VW parts book says 125 main jet |
| VW 324-2 | 31PICT-3 | 113905205AK | Ghia | 1300 | 1971 | 120 |  | 65 | Non-US autostick Aux fuel jet-50, M527 VW parts book says 125 main jet |
| VW 325-2 | 34PICT-3 | 113905205AN | Bug | 1600 | 8/70 | 127.5 | 75z | 60 | USA Manual Aux Fuel 42.5 |
| VW 325-3 | 34PICT-3 | 113905205AN | Bug | 1600 | 8/71 | 127.5 | 75z | 55 | California manual Aux Fuel 42.5 Generator accelerator pump |
| VW 325-4 | 34PICT-3 | 113905205AN | Bug | 1600 | 1973 | 127.5 | 75z |  | California manual Alternator accelerator pump |
| VW 326-1 | 34PICT-3 | 113905205AJ | Ghia | 1600 | 1972 | 127.5 | 80z | 60 | USA manual |
| VW 326-3 | 34PICT-3 | 113905205AN | Ghia | 1600 | 8/71 | 12705 | 70z | 55 | USA manual to AE 628298 Aux Fuel 42.5 |
| VW 327-1/2 | 34PICT-3 | 211905205Q | BUS | 1600 | 1971 | 125 | 60z | 57.5 | USA |
| VW 328-1 | 34PICT-3 | 113905205AJ | Bug | 1600 | 08/70 | X130 | 60Z | 65 | Non-US manual AD engine, M527 |
| VW 329-1 | 34PICT-3 | 113905205AK | Bug | 1600 | 08/70 | X130 | 60Z | 65 | Non-US autostick AD engine, M527 |
| VW 330-1 | 34PICT-3 | 113905205AJ | Ghia | 1600 | 08/70 | X130 | 80Z | 65 | Non-US manual AD engine, M527 |
| VW 331-1 | 34PICT-3 | 113905205AK | Ghia | 1600 | 08/70 | X130 | 80Z | 65 | Non-US autostick AD engine, M527 |
| VW 332-1 | 34PICT-3 | 211905205R | BUS | 1600 | 1971 | 125 | 60z | 60 | M527 |
| VW 343-2/3 | 34PICT-3 | 113908205AH | Bug | 1600 | 8/71 | 127.5 | 75z | 55 | California Autostick Aux Fuel 42.5 Generator accelerator pump |
| VW 341 | 31PICT-3 |  | Bus | 1300 | 03/71 |  |  |  | Italy 1300DP Type 2 |
| VW 343-4 | 34PICT-3 | 113908205AH | Bug | 1600 | EARLY/MID 1973 | 127.5 | 75z | 55 | California autostick Alternator accelerator pump DISTRIBUTOR CHANGED AT AH0098884 |
|  |  | 043905205D |  |  | late 73 |  |  |  |  |
| VW 344-2 | 34PICT-3 | 113905205AH | Ghia | 1600 | 08/71 | 127.5 | 70z | 55 | California Autostick Aux Fuel 42.5 |
| VW 355-1 | 34PICT-3 | 113905205AJ | Bug | 1600 | 01/06/71 | X130 | 60Z | G65 | Non-US manual AD engine aux fuel 42.5 FROM ENG AD257544-AD360022. |
| VW 355-2 | 34PICT-3 | 113905205AL 043905205 | Bug | 1600 | 08/71 | X130 | 60Z | G55 | Non-US manual AD engine FROM ENG AD360023 aux fuel 42.5 |
| VW 355-3 | 34PICT-3 | 043905205 | Bug | 1600 | 08/71 | 130 | 60z | 55 | Non-US manual AS engine, PAPER AIR CLEANER aux fuel 42.5 |
| VW 356-1 | 34PICT-3 | 113905205AK | Bug | 1600 | 08/71 | 130 | 60z | 55 | Non-US autostick AD AF and AS ENG AD257544-AD360022 aux fuel 42.5 |
| VW 356-2 | 34PICT-3 | 113905205AM 043905205A | Bug | 1600 | 08/71 | 130 | 60z | 55 | Non-US autostick AD AF and AS , FROM ENG AD360023 aux fuel 42.5 |
| VW 356-4 | 34PICT-3 | 043905205A | Bug | 1600 | 08/71 | 130 | 60z | 55 | Non-US autostick AD/AS engine, FROM ENG AD360024+AS aux fuel 42.5 |
| VW 357-1,2,3 | 34PICT-3 | 113905205AJ | Ghia | 1600 | 08/71 | X130 | 80Z | 65 | Non-US MANUAL AD, AF and AS engine, ENG AD257544-AD360022 |
| VW 357-2 | 34PICT-3 | 113905205AL 043905205 | Ghia | 1600 | 08/71 | X130 | 80Z | 55 | Non-US MANUAL AD engine, FROM ENG AD360023 |
| VW 358-1 | 34PICT-3 | 113905205AK | Ghia | 1600 | 08/71 | X130 | 80Z | 65 | Non-US AUTO AD AF and AS engine, ENG AD257544-AD360022 |
| VW 358-2 | 34PICT-3 | 113905205AM 043905205A | Ghia | 1600 | 08/71 | X130 | 80Z | 55 | Non-US AUTO AD engine, FROM ENG AD360023 |
| VW 359-1 | 34PICT-3 | 113905205AL | BUS | 1600 | 08/71 | X125 | 60Z | G60 | Non-US manual AD and AS engine, ENG AD290641-AD350045 |
| VW 359-2 | 34PICT-3 | 211905205S 043905205B (AS eng) 181905205 | BUS 181 | 1600 | 08/71 | X125 | 60Z | G55 | Non-US manual AD engine, FROM ENG AD350046 &AS eng M632/623 |
| VW 360-1,2 | 31PICT-3 | 113905205AL | Bug | 1300 | 08/71 | 130 | 110z | 52.5 | Non-US manual Aux fuel jet-45, FROM ENG AB350001 |
| VW 361-1,2,3 | 31PICT-3 | 113905205AM | Bug | 1300 | 08/71 | 130 | 110z | 52.5 | Non-US autostick Aux fuel jet-45, FROM ENG AB350001 |
| VW 362-1 | 31PICT-3 | 113905205AL | Ghia BUS | 1300 | 01/71 | 130 | 110z | g60 | Non US Aux fuel jet - 50 FROM ENG AB 155180 (Ghia) Also Italian-Spec BUS M252 VW parts book says 125 main 140z AC |
| VW 362-2 | 31PICT-3 | 113905205AL | Ghia BUS | 1300 | 1972 | 130 | 125z | 60 | Non-US manual Aux fuel jet-45, FROM ENG AB155180 M252 VW parts book says 125 main 140z AC |
| VW 363-1 | 31PICT-3 | 113905205AM | Ghia | 1300 | 1972 | 125 | 140z | 65 | Non-US Autostick VW parts book says 125 main 140z AC |
| VW 363-2,3 | 31PICT-3 | 113905205AM | Ghia | 1300 | 08/71 | 130 | 125z | 60 | Non-US autostick, aux fuel 45 FROM ENG AB350001 VW parts book says 125 main 140z AC |
| VW 364-1,2 | 31PICT-3 | 113905205AL | Bug | 1300 | 08/71-11/72 | 130 | 110z | 55 | Non-US Manual 6V |
| VW 365-1 | 31PICT-3 | 113905205AL | 181 | 1300 | 1972 | 130 | 110z | g65 | Non-US Thing AG002099 - AG003000 |
| VW 365-2 | 31PICT-3 | 113905205AL | 181 | 1600 | 08/71 | 125 | 110z | 55 | Non-US Thing AG engine aux fuel 45 AG003001- |
| VW 366-1 | 31PICT-3 | 181905205 | 181 | 1600 | 8/71 | x125 | 110z | 55 | Non US Thing M63 aux fuel 45 |
| VW 367-1 | 34PICT-3 | 113905205AL 181905205 | BUS | 1600 | 08/71 | X125 | 60Z | G60 | Non-US manual AD290641-AD350045 (with M623 M632) |
| VW 367-2 | 34PICT-3 | 211905205S 043905205B (AS eng) | BUS | 1600 | 08/71 | X125 | 60Z | G55 | Non-US manual AD engine, FROM ENG AD350046 & AS eng |
| VW 377-1 VW 377-2 | 34PICT-3 | 113905205AN | Bug | 1600 | 11/71 | 127.5 | 75z | 55 | USA Manual Aux Fuel 42.5 |
| VW 378-1 | 34PICT-3 | 113905205AN | Ghia | 1600 | 11/71 | 127.5 | 70z | 55 | USA Manual From AE 627299 Aux Fuel 42.5 |
| VW 390-1 VW 390-2 | 31PICT-4 | 043905205 | Bug | 1300 | 11/72-8/73 | x130 | 110z | 52.5 | Non US Manual aux fuel 45 paper air cleaner |
| VW 394-1 VW 394-2 | 31PICT-4 | 043905205A | Bug | 1300 | 1973 | x130 | 110z | 52.5 | Non US Autostick aux fuel 45 |
| VW 395 | 31PICT-4 |  |  |  | 11/72-6/73 | 130 | 110z | 52.5 | Non US 6V |
| VW 401-1 | 34PICT-3 | 043905205 | 181 | 1600 | 4/73 | x127.5 | 75z | 55 | Non US Thing aux fuel 47.5 |
| VW 402-1 | 34PICT-3 | 043905205 | 181 | 1600 | 4/73 | x127.5 | 75z | 55 | Non US Thing M63 aux fuel 47.5 |
| VW 404-1 | 34PICT-3 | 043905205 | 181 | 1600 | 3/73 | x127.5 | 75z | 55 | US Thing M157 aux fuel 47.5 |
| VW 410-1 | 34PICT-3 | 113905205AN 043905205 | Bug | 1600 | 1973 | 127.5 | 70z | 55 | USA Manual (one source states this could be a DVDA setup, but I suspect they were all set up for SVDA) |
| VW 411-1 | 34PICT-3 | 113905205AN 043905205C | Bug | 1600 | 1973 | 127.5 | 75z | 55 | California manual |
| VW 412-1 | 34PICT-3 | 113908205AH 043905205A | Bug | 1600 | 1973 | 127.5 | 75z | 55 | USA and Japan Autostick (one source states this could be a DVDA setup, but I suspect they were all set up for SVDA) |
| VW 427-1 | 34PICT-3 | 043905205 | Bug | 1600 | 1974 | 127.5 | 70z | 55 | USA Manual |
| VW 428-1 | 34PICT-3 | 043905205A | Bug | 1600 | 1974 | 127.5 | 75z | 55 | USA and Japan Autostick |
| VW 429-1 | 34PICT-4 | 043905205C | Bug | 1600 | 1974 | 127.5 | 60z | 55 | California manual Aux Fuel 47.5 |
| VW 430-1 | 34PICT-4 | 043905205A | Bug | 1600 | 1974 | 127.5 | 60z | 55 | California autostick Aux Fuel 47.5 |
| VW 431-1 | 34PICT-3 | 043905205 | Ghia | 1600 | 1974 |  |  |  | USA Manual |
| VW 449-1 | 31PICT-4 | 043905205 | Bug | 1300 | 08/73-6/77 | 130 | 110z | 52.5 | Non-US manual AR engine aux fuel 45 paper air cleaner |
| VW 450-1 | 31PICT-4 | 043905205A | Bug | 1300 | 08/73 | 130 | 110z | 52.5 | Non-US autostick AR engine aux fuel 45 |
| VW 459-1 | 34PICT-3 |  | BUG | 1600 | 08/73 | 127.5 | 75z | 55 | Japan manual aux fuel 47.5 |
| VW 460-1 | 34PICT-3 |  | BUG | 1600 | 08/73 | 127.5 | 75z | 55 | Japan Autostick aux fuel 47.5 |
| VW 461-1 | 34PICT-3 |  | Ghia | 1600 | 08/73 | 127.5 | 70z | 55 | Japan Manual aux fuel 47.5 |
| VW 462-1 | 34PICT-3 |  | Ghia | 1600 | 08/74 | 127.5 | 70z | 55 | Japan Autostick aux fuel 47.5 |
| VW 471 | 30PICT-3 | 043905205 | Bug | 1200 | 06/74 | 112.5 | 170w | 50 | Non-US 1200 6V aux fuel jet 40 |
| VW 472-1 | 30PICT-3 | 043905205 | Bug | 1200 | 06/74 | 112.5 | 170w | 50 | Non-US 1200 FROM D1268063 12V Aux fuel jet 40 |
| VW 489-1 | 34PICT-4 |  |  | 1600 | 08/74 | 127.5 | 75z | 55 | Japan aux fuel 47.5 |
| VW 510-1 | 34PICT-3 |  |  | 1600 | 08/75 |  | 60z | 55 | Japan Manual aux fuel 47.5 |
| VW 522 | 34PICT-3 |  | 181 |  | 09/75 |  |  |  | Non-US |
| VW 523-1,2,3 | 34PICT-4 | 043905205 K | Bug | 1600 | 08/75 | 127.5 | 60z | 55 | Non-US manual AS engine aux fuel 47.5 |
| VW 524-1,2,3 | 34PICT-4 | 043905205 A | Bug | 1600 | 08/75 | 127.5 | 60z | 55 | Non-US autostick AS engine aux fuel 47.5 |
| VW 525-1/3/4 | 30PICT-3 | 043905205 K | Bug | 1200 | 08/75 | 112.5 | 170w | 47.5 | European 1200 , aux fuel 40 12V FROM ENG D1347143, M88 |
| VW 527-1 | 34PICT-3 | 043905205 L | BUS | 1600 | 08/75 | 125 | 80z | 55 | Non-US AS engine aux fuel 47.5 |
| VW 533 | 34PICT-3 |  | 181 |  | 09/75 |  |  |  | Non-US |
| VW 536 | 34PICT-3 |  | BUS | 1600 | 09/75 |  |  |  | Non-US |
| VW 538 | 34PICT-3 |  | BUS | 1600 | 09/75 |  |  |  | Non-US “Dust-Proof” |
| NOTE about the replacement Brazil made Brosol H30/31PICT Carburetor. It may look like is set up for SVDA or DVDA but the traditional vacuum fitting on the left side of the carb is actually set up for the SVA “Vacuum Only” style distributors used mostly up through model year 1970. However this carburetor has 4 vacuum ports and one of them does actually work for SVDA/DVDA advance. However, it is the one furthest away from the distributor… it’s the upward-angled fitting at the right rear of the carburetor. In accessing this fitting one must take care that the vacuum line be routed out of range of movement of the throttle arm. |
| N/A | L-Jet EFI | 043905205H | Bug | 1600 | 08/74 | Fuel Injected Manual Trans USA - Idle Timing 5ATDC |
| N/A | L-Jet EFI | 043905205J | Bug | 1600 | 08/74 | Fuel Injected Autostick Trans USA - Idle Timing 0TDC |
| (data in red added by my collaborator Andrew Paroczy , in blue and pink are most recent additions by Andy T.) data in orange are carbs reported to me to exist by people, but have yet to find any documentation regarding them. |
| Distributor part number cross reference – VW to Bosch |
| 043 905 205 | 0 231 170 034 | 111 905 205 N | 0 231 137 005 ZV/JU4R6 | 113 905 205 AD | 0 231 167 012 |
| 043 905 205A | 0 231 170 036 | 111 905 205 T | 0 231 137 029 | 113 905 205 AE | 0 231 167 029 |
| 043 905 205B | 0 231 168 001 | 111 905 205 AA | 0 231 137 039 |  |  |
| 043 905 205C | 0 231 176 028 |  |  | 113 905 205 AH | 0 231 167 053 |
| 043 905 205D | 0 231 176 033 | 113 905 205 A | ZV/PAU 4R2 0 231 139 002 | 113 905 205 AJ | 0 231 167 049 |
| 043 905 205H | 0 231 176 044 | 113 905 205 A | ZV/PAU 4R5 0 231 139 005 | 113 905 205 AK | 0 231 167 051 |
| 043 905 205J | 0 231 176 053 |  |  | 113 905 205 AL | 0 231 146 101 |
| 043 905 205K | 0 231 170 186 | 113 905 205 K | 0 231 137 009 | 113 905 205 AM | 0 231 115 094 |
| 043 905 205L | 0 231 168 015 | 113 905 205 L | 0 231 137 010 | 113 905 205 AN | 0 231 167 070 |
|  |  | 113 905 205 M | 0 231 137 021 |  |  |
|  |  | 113 905 205 P | 0 231 115 056 | 211 905 205E | 0 231 129 019 VJ 4 BR 8 |
| 111 905 205 C | 0 231 115 040 VJU4BR8 | 113 905 205 T | 0 231 137 035 | 211 905 205F | 0 231 129 010 VJR 4 BR 25 |
| 111 905 205 H | 0 231 138 001 ZV/PAU4R1 |  |  | 211 905 205N | 0 231 137 027 |
| 111 905 205 L 111 905 205 M | ZV/JU4R3 0 231 147 002 | 113 905 205 AA | 0 231 115 078 | 211 905 205P | 0 231 137 037 |
|  |  | 113 905 205 AC | 0 231 115 082 | 211 905 205Q | 0 231 173 001 |
|  |  |  |  | 211 905 205 S | 0 231 180 001 |
| Special thanks to Andrew Paroczy (1500king on TheSamba) and the late Moby5153 on the British VZi Forums for much of the Non-USA information, and to TheSamba.com archives for the other dates, including the 1967/earlier VW Technical Bulletin Engine data supplements (http://www.thesamba.com/vw/archives/manuals/techbulletins/m1.php) that much of this information was compiled from, plus the German-language “Technische Merkblätters” formerly (dead link) at: http://vwbus2.dyndns.org/bulli/michaelk/vw_bus_d/tm_k/frame.html as well as some found on VW’s website http://www.volkswagen-classic.de/en/classic-parts/service/reparaturleitfaden/typ-1-1975-85 - and some of the DVG-Pierburg Solex records found at www.ruddies-berlin.de. Originally this chart began as I compiled the data from JT Garwood’s Car of the Century yearly carb and distributor charts. |
| This is not a complete listing. Anyone with additional or missing information that could be added to this chart, email me at glutamodo@aol.com. Technical bulletins regarding engine data from 1968 and newer are especially desired. – Andy T. Last updated NOV 20, 2020 |